## Slide 1
Sreenidhi Institute of Science and Technology, Hyderabad
Department of Electronics & Communication Engineering
Edge AI (TinyML) Based Condition Monitoring
and Fault Detection of Engines
Using MEMS Sensors and ESP32
Major Project Report | B.Tech ECE | 2025–2026
Submitted by
Bollagoni Pavan Kumar (22311A04F7)
KothiRithish (22311A04F6)
Enaganti Neha (22311A04F0)
Under the guidance of
Prof. Shruthi Bargav
Assistant Professor, Dept. of ECE, SNIST

## Slide 2
Abstract
Engine faults such as rotor imbalance, shaft misalignment, and bearing wear cause costly unplanned industrial downtime — early detection through continuous monitoring is critical for both safety and production continuity.
Conventional cloud-based monitoring systems suffer from high latency (1–5 seconds), excessive bandwidth consumption, and complete operational failure during network outages.
This project deploys a TinyML neural network classifier on a Seeed XIAO ESP32-S3 microcontroller, using an INMP441 MEMS microphone for real-time, on-device acoustic fault classification.
MFCC features (13 cepstral coefficients, 728-element vector) are extracted from 1-second audio windows and classified into four engine states: Normal, Knock/Misfire, Pressure Anomaly, and Bearing Wear.
The EON Compiler quantised model achieves 81.3% validation accuracy, 93–96% live test accuracy, 3 ms inference time, and 46.2 KB flash footprint — entirely without cloud connectivity.
2 / 11

## Slide 3
Literature Survey
Reference | Platform | Accuracy | Inference | Key Limitation
Gultekin et al., Sensors 2022 | Raspberry Pi 4 | 93.5% | ~200 ms | High cost, high latency
TinyML-Edge CNN, Ex. Sys. 2023 | STM32H7 | 91.8% | ~65 ms | Higher-spec MCU required
Ma et al., IEEE TII 2022 | ARM Cortex-M4 | 89.2% | ~80 ms | No power analysis
Bhushan et al., Sci. Rep. 2025 | ESP32-S3 | 88.1% | ~12 ms | No EON optimisation
Hymel et al., arXiv 2022 | Edge Impulse | — | — | Platform description only
Warden & Situnayake, 2020 | Various MCUs | — | — | Foundational reference
Research Gap
No complete, validated end-to-end TinyML pipeline on ESP32-class microcontrollers with published on-device hardware measurements, power analysis, and comparison against related works.
3 / 11

## Slide 4
Objectives
1.
Build a real-time acoustic sensor node using INMP441 MEMS microphone and XIAO ESP32-S3 for continuous engine signal capture at 16 kHz sampling rate.
2.
Collect and curate a labelled dataset of four engine fault classes using the Edge Impulse data acquisition pipeline.
3.
Configure an MFCC DSP pipeline (13 coefficients, 32 Mel filters, 512-pt FFT) producing a 728-element feature vector per 1-second window.
4.
Design and train a compact dense neural network (128→64→32) achieving over 80% validation accuracy within ESP32 memory constraints.
5.
Deploy via the EON Compiler with int8 quantisation targeting less than 50 KB flash, 15 KB RAM, and 10 ms inference latency.
6.
Evaluate the deployed system against classification accuracy, on-device latency, memory usage, power consumption, and four published benchmark works.
4 / 11

## Slide 5
Methodology — System Architecture
Development Phase
Edge Impulse Cloud Platform
1. Data Acquisition via Wi-Fi
2. Dataset Management & QA
3. Impulse Design (Audio Input)
4. MFCC DSP Configuration
5. Neural Network Training (100 epochs)
6. EON Compiler Arduino Library Export
Deploy
Deployment Phase
XIAO ESP32-S3 — No Internet Required
1. I2S DMA Audio Capture (16 kHz)
2. MFCC Feature Extraction (~350 ms)
3. TinyML Neural Network Inference (3 ms)
4. Confidence Threshold Check (0.6)
5. OLED Display Update (500 ms cycle)
6. Optional MQTT / Wi-Fi Status Upload
5 / 11

## Slide 6
Methodology — Hardware & Feature Extraction
Hardware Components
Component | Specification
XIAO ESP32-S3 | Dual LX7 @ 240 MHz, 8 MB flash/PSRAM
INMP441 MEMS Mic | I2S, 61 dBFS SNR, 60 Hz–15 kHz
SSD1306 OLED | 128×64 px, I2C, ~10 mA
LiPo Battery | 3.7 V, 1200 mAh, ~10 hrs runtime
EON Compiler | 46.2 KB flash, 12.5 KB RAM, 3 ms
Total hardware cost: approximately 2,000 rupees
MFCC Processing Pipeline
1
Pre-Emphasis Filter
High-pass (α=0.97)
2
STFT + Hamming Window
512-pt FFT, 20 ms frames
3
32 Mel Filterbank
Perceptual frequency scaling
4
Log Compression
Dynamic range reduction
5
DCT → 13 Coefficients
728-element feature vector
Key MFCC Parameters
Parameter | Value | Parameter | Value
Coefficients | 13 | Mel Filters | 32
FFT Length | 512 pts | Frame Size | 20 ms
Frequency Range | 0–8 kHz | Feature Vector | 728 values
6 / 11

## Slide 7
Methodology — Neural Network & Deployment
Network Architecture (~110,000 parameters)
Input
728
Dense 1
128 · ReLU
Dropout 25%
Dense 2
64 · ReLU
Dense 3
32 · ReLU
Output
4 · Softmax
Training Configuration
Parameter | Value
Epochs | 100
Optimiser | Adam (LR 0.005)
Loss Function | Categorical Cross-Entropy
Batch Size | 32
Dropout | 25% on first hidden layer
Data Augmentation | Disabled
EON Compiler Deployment
Metric | Value
Inference Time | 3 ms
Flash Usage | 46.2 KB
Peak RAM | 12.5 KB
Flash vs. TFLite | 49% reduction
RAM vs. TFLite | 40% reduction
Accuracy Impact | < 1% degradation
7 / 11

## Slide 8
Results
Validation Accuracy: 81.3% | AUC-ROC: 0.85 | Precision: 0.82 | Recall: 0.81
Chart: Per-Class Live Inference Accuracy (%)
| Normal (noise) | Knock (highcough) | Bearing (sneeze) | Misalignment (snoring)
Live Accuracy (%) | 96 | 94 | 95 | 93
Validation F1 Scores
Class | F1 Score
Normal (noise) | 0.78
Knock (highcough) | 0.67
Pressure (sneeze) | 0.50
Bearing (snoring) | 0.88
Note: sneeze class F1 = 0.50 due to only 8 training samples.
Expected to exceed 0.75 with 30+ samples collected.
End-to-end detection latency: ~500 ms | Inference: 3 ms | Flash: 46.2 KB | RAM: 12.5 KB | Battery: ~10 hrs continuous
8 / 11

## Slide 9
Results — Comparison with Published Works
Reference | Platform | Accuracy | Inference | Cost Level
Gultekin et al., 2022 | Raspberry Pi 4 | 93.5% | ~200 ms | High
TinyML-Edge CNN, 2023 | STM32H7 | 91.8% | ~65 ms | Medium
Ma et al., 2022 | ARM Cortex-M4 | 89.2% | ~80 ms | Medium
Bhushan et al., 2025 | ESP32-S3 | 88.1% | ~12 ms | Low
This Work | XIAO ESP32-S3 | 94.5% (live) | 3 ms | ~INR 2,000
Key Findings
Lowest reported inference latency (3 ms) among all compared works on any embedded platform.
Highest live test accuracy (94.5%) achieved on ESP32-class microcontroller hardware.
Hardware cost 15–200 times lower than equivalent commercial vibration monitoring solutions.
9 / 11

## Slide 10
Conclusion & Future Scope
Conclusion
1.
Complete TinyML pipeline successfully deployed and validated on real XIAO ESP32-S3 hardware — 81.3% validation accuracy, 93–96% live test accuracy, with all metrics measured on actual hardware.
2.
EON Compiler achieves 3 ms inference — 5 times faster than standard TFLite — the ESP32 spends just 0.6% of its cycle time on neural network computation.
3.
Deployed model occupies 46.2 KB flash and 12.5 KB RAM, with total system draw of 96 mA enabling 10–11 hours continuous monitoring from a 1200 mAh LiPo battery.
4.
Total hardware cost of approximately 2,000 rupees — 15 to 200 times lower than commercial vibration monitoring solutions — makes fleet-scale predictive maintenance economically viable.
Future Scope
Multi-sensor fusion — integrate MPU-6050 accelerometer for vibration + acoustic combined classification.
Expanded dataset — target 500+ samples per class across multiple motor types and operating conditions.
Over-the-air firmware updates and industrial protocol integration (Modbus TCP, OPC-UA, MQTT).
10 / 11

## Slide 11
References
[1] Bhushan C. M. et al., "Deploying TinyML for Energy-Efficient Object Detection," Scientific Reports, vol. 15, 2025.
[2] Gultekin O. et al., "Real-Time Fault Detection Using Edge AI," Sensors, vol. 22, no. 14, 2022.
[3] Hymel S. et al., "Edge Impulse: An MLOps Platform for Tiny Machine Learning," arXiv:2212.03332, 2022.
[4] Zhang X. et al., "Hardware-Algorithm Co-Design for Efficient TinyML Systems," ACM TECS, 2022.
[5] Ma S. et al., "Privacy-Preserving Anomaly Detection in Industrial Systems Using Edge AI," IEEE TII, vol. 18, 2022.
[6] Warden P. and Situnayake D., TinyML — O'Reilly Media, 2020.
[7] Randall R. B. and Antoni J., "Rolling Element Bearing Diagnostics," Mech. Syst. Signal Process., vol. 25, 2011.
[8] David R. et al., "TensorFlow Lite Micro: Embedded ML on TinyML Systems," MLSys, vol. 3, 2021.
[9] Shi W. et al., "Edge Computing: Vision and Challenges," IEEE IoT Journal, vol. 3, no. 5, 2016.
[10] Xu C. et al., "On-Device Learning for Edge AI: A Survey," IEEE Access, vol. 10, 2022.
Thank You
We welcome your questions
11 / 11